## Slide 1: Determination of uranium in hair samples
Postgraduate Educational Course in Radiation Protection and the Safety of Radiation Sources
Supervisor:
Dr. K. Kehagia
Environmental Radioactivity Department
Greek Atomic Energy Commission
Sofia C. Papadopoulou
Biologist

## Slide 2
Introduction

## Slide 3
The element uranium (U)
Natural primordial radioactive heavy metal
Present in mineral deposits (e.g. granites, uraninite rocks)
Erosion of minerals results in the mobility of U in environment
Presence in water and soil
Absorbed by plants and enter the food chain
Human intake of uranium by water and food
www.atomicheritage.org/history/uranium-mining

## Slide 4
Health effects of U
As heavy metal poses chemical toxicity hazards (nephrotoxic)
Radioactive element results in potential radiological effects (lower importance)

## Slide 5
Radiochemical analysis in a biological material (such as this!)
Alpha spectrometry
Subject of project work:
In order to familiarize with
But why hair???
Determination of U levels in hair by alpha spectrometry

## Slide 6
Hair could be an indicator of uranium chronic exposure
U transfer and accumulation in hair during growth
Bioindicator of U long time after exposure
Advantage over urine analysis (acute exposure indicator)

## Slide 7
Materials and Methods

## Slide 8
Materials and Methods
Sample collection
Sample pretreatment
Uranium separation
Source preparation
Counting by alpha spectrometry

## Slide 9
Materials and Methods
Sample collection
Sample pretreatment
Uranium separation
Source preparation
Counting by alpha spectrometry

## Slide 10
1. Sample collection
Materials and Methods
7 healthy volunteers from
Group of study:
Bosnia and Herzegovina
Portugal
Greece
United Kingdom
Australia

## Slide 11
Materials and Methods
Hair collection from the occipital part of head  1-3 g
2. Sample collection

## Slide 12
Materials and Methods
Sample collection
Sample pretreatment
Uranium separation
Source preparation
Counting by alpha spectrometry

## Slide 13
1. Sample pretreatment
Sample weighing
Spike with 0.5 ml 232U
(0.012Bq/ml)
Wet ashing
HNO3 + HCl (18-24 ml)

## Slide 14
2. Sample pretreatment
After wet ashing…
Dry ashing (500 C, 6 hours)
…after dry ashing

## Slide 15
Materials and Methods
Sample collection
Sample pretreatment
Uranium separation
Source preparation
Counting by alpha spectrometry

## Slide 16
3. Uranium separation
Ion exchange
chromatography
4. Source preparation
Electrodeposition
on stainless steel disk
Uranium source

## Slide 17
Materials and Methods
Sample collection
Sample pretreatment
Uranium separation
Source preparation
Counting by alpha spectrometry

## Slide 18
5. Counting by alpha spectrometry
Counting for 5 days
Integrated alpha spectroscopic system (Canberra)
with 12 passivated implanted planar silicon (PIPS) detectors

## Slide 19
Results

## Slide 20
Sample | Gender | Country | 238U (mBq/g) | 234U (mBq/g) | 234U/238U | 238U (ng/g)
S1 | F | B&H | 0.16 ± 0.06 | 0.23 ± 0.07 | 1.42 | 12.9 ± 4.6
S2 | F | PT | 0.39 ± 0.09 | 0.85 ± 0.14 | 2.16 | 31.7 ± 7.5
S3 | F | GR | 0.13 ± 0.03 | 0.18 ± 0.03 | 1.31 | 10.7 ± 2.3
S4 | M | GR | 0.12 ± 0.02 | 0.21 ± 0.04 | 1.83 | 9.2 ± 2.0
S5 | M | GR | 0.89 ± 0.09 | 0.87 ± 0.1 | 0.98 | 71.9 ± 7.7
S6 | F | AUS | < LD | 0.46 ± 0.09 | - | -
S7 | F | UK | 0.46 ± 0.07 | 0.45 ± 0.08 | 0.96 | 37.4 ± 5.9
Chemical recovery: 59.6-70.6 %
Uncertainties: 1σ

## Slide 21
Chart: U-238 and U-234 specific activities
| S1 | S2 | S3 | S4 | S5 | S6 | S7
U-238 | 0.16043 | 0.39426 | 0.13335 | 0.11457 | 0.89478 | 0.13843 | 0.46543
U-234 | 0.22746 | 0.85229 | 0.17452 | 0.21022 | 0.87401 | 0.46599 | 0.44823

## Slide 22
Spectrum of sample 5

## Slide 23
Discussion

## Slide 24
Comparison of our results to other studies
Country (Year) | U (ng/g)
Slovenia (1991) | 2.3-33
Sweden (2000) | 6-436
Balkan area (2012) | 0.9-449
Serbia (2015) | 0.25-77
Greece (2010) | 12-170
Balkan region (PGEC 2014) | 11-54
Finland (2007) | 18,000-821,000
Finland (2005) | 6.5-250,000
ICRP 23 reported value | 130
Several regions (our study) | 9.2-71.9

## Slide 25
Chart: Uranium Concentration (ng/g)
| ICRP 23 reported value | Several regions (our study) | Balkan region (2012) | Balkan region (PGEC 2014) | Slovenia (1991) | Serbia (2015) | Greece (2010) | Sweden (2000) | Finland (2005) | Finland (2007)
 | 130 | 9.2 | 0.9 | 11 | 2.3 | 0.25 | 12 | 6 | 6.5 | 18000
 | 20 | 62.7 | 448.1 | 43 | 30.7 | 76.75 | 158 | 430 | 249993.5 | 803000

## Slide 26
Conclusions

## Slide 27
Satisfactory chemical recovery (hair: complex biological material)
Uranium levels of our study:
Conclusions
In accordance with international literature and below reported value of ICRP 23
Lower than those of studies in high U background
Activity ratios of 234U/ 238U comparable with literature

## Slide 28
References
A. R. Byrne and L. Benedik, “Uranium content of blood,urine and hair of exposed and non-exposed persons determined by radiochemical neutron activation analysis, with emphasis on quality control,” The Science of Total Environment, vol. 107, pp. 143–157, 1991.
A. Israelsson and H. Pettersson, “Measurements of 234U and 238U in hair, urine and drinking water among drilled bedrockwell water users for the evaluation of hair as a biomonitor of uranium intake,” Health Physics Society, vol. 107, no. 2, 2014.
Z. Karpas, O. Paz-Tal, A. Lorber et al., “Urine, hair and nails as indicators for ingestion of uranium in drinking water,” Health Physics Society2, vol. 88, no. 3, pp. 229–242, 2005.
K. Kehagia, S. Bratakos, M. Kolovou et al., “Hair analysis as an indicator of exposure to uranium,” Radiation ProtectionDosimetry, pp. 1–4, 2010.
M. Muikku, T. Heikkinen, M. Puhakainen et al., “Assessment of occupational exposure to uranium by indirect methods need information on natural background variations,” Radiation Protection Dosimetry, vol. 125, pp. 492–495, 2007.
I. Rodushkin and M. Axelsson, “Application of double focusing sector field ICP-MS for multielemental characterization of human hair and nails. Part II. A study of the inhabitants of northern Sweden,” The Science of Total Environment, vol. 262, pp. 21–36, 2000.
S. K. Sahoo and Z. S. Zuni, “Distribution of uranium, thorium and some stable trace and toxic elements in human hair and nails in Ni ska Banja Town, a high natural background radiation area of Serbia (Balkan Region, South-East Europe),” Journal of Environmental Radioactivity, vol. 145, pp. 66–77, 2015.
B. Seslak, “Urine and hair analysis as an indicator of exposure to uranium,” PGEC, 2014.
Z. S. Zunic, S. Tokonami, S. Mishra et al., “Distribution of uranium and some selected trace metals in human scalp hair from balkans,” Radiation Protection Dosimetry, vol. 152, pp. 220–223, 2012.

## Slide 29

Thank you for your attention…!